## Slide 1: RIT-Magnetism & Its Applications
Fsc RIT
AWAIS HAMZA

## Slide 2: Electromagnetic Induction
Electromagnetic induction is the production of an induced EMF when magnetic flux through a circuit changes.
Basis of generators, transformers, induction motors, inductors.
Magnetic flux (Φ) changes due to:
Change in magnetic field
Change in area
Change in orientation

## Slide 3: Faraday’s Law of Electromagnetic Induction
The induced EMF is directly proportional to the rate of change of magnetic flux.
Faraday’s Law:
“N” = number of turns
Negative sign shows opposing nature of induced EMF (Lenz’s law).
Faster change = larger EMF.

## Slide 4: Lenz’s Law
The direction of induced EMF is such that it opposes the change that produced it.
Demonstrated by the negative sign in Faraday’s law.
Explains:
Opposing currents in coils
Magnetic braking
Induced currents resisting motion

## Slide 5: Self-Induction
When current in a coil changes, the coil induces an EMF in itself.
This induced EMF opposes change in current.
The property of a coil to induce EMF in itself is called self-inductance (L).
Formula:

## Slide 6: Mutual Induction
When current changes in one coil, it induces an EMF in another nearby coil.
Basis of transformers, wireless charging, induction cookers.
Mutual inductance depends on:
Number of turns
Distance between coils
Core material (iron increases induction)

## Slide 7: Eddy Currents
When a solid conductor is placed in a changing magnetic field, circular currents are produced.
These circulating currents are called eddy currents.
Effects:
  Heating of metals
  Power loss in transformers
  Magnetic braking in trains
Reduced by:
  Laminated iron cores
  Slotted cores

## Slide 8: Transformers
A transformer changes AC voltage from one level to another.
Works on mutual induction.
Two coils:
  Primary coil (input AC)
  Secondary coil (output AC)
Types
Step-up: increases voltage
Step-down: decreases voltage
Transformer Equation

## Slide 9: Transformer Components
Iron core: increases magnetic flux
Primary coil
Secondary coil
Insulation
Tank with cooling oil
Laminated core (reduces eddy currents)

## Slide 10: Ideal Transformer
No energy losses
100% efficiency
No eddy currents, heat losses, flux leakage
Power conservation:

## Slide 11: Introduction to AC (Alternating Current)
AC changes direction and magnitude continuously.
Represented by a sine wave.
AC quantities:
Amplitude
Frequency
Time period
RMS values

## Slide 12: Tesla’s Polyphase System
Introduced by Nikola Tesla.
Uses three-phase AC.
Advantages:
  Smooth rotation in motors
  Higher efficiency
  Less power loss
  Self-starting motors
Used in:
Power plants
Industry
Transmission systems

## Slide 13: Power Grid Distribution
Steps:
Generation (power stations)
Step-up transformers (very high voltage transmission)
Transmission lines
Step-down transformers at grid stations
Distribution to homes and industries
Reason for using high voltage
Reduces current
Reduces power loss

## Slide 14: Transformer Theory
Based on mutual induction.
Changing AC current in primary produces changing magnetic flux in the core.
This flux links with secondary coil → induces EMF.
Efficiency affected by:
  Copper losses
  Eddy current losses
  Hysteresis losses
  Flux leakage

## Slide 15: Current Transformation (Current Ratio)

## Slide 16: Working Principle of a Transformer (Recap)
AC in primary coil → produces alternating magnetic flux in core.
Flux links the secondary coil → by mutual induction an EMF is induced.
Secondary EMF magnitude depends on turns ratio and rate of flux change.
Requires AC supply (no steady DC operation).

## Slide 17: Transformer Core & Core Medium
Purpose: Provide low reluctance path for magnetic flux and improve coupling.
Core materials:
Laminated silicon steel (power transformers) — reduces eddy currents.
Amorphous metal (low core losses) — used for energy-efficient transformers.
Ferrite cores (high frequency devices, e.g., SMPS) — low eddy & hysteresis at high freq.
Core shapes / types: core-type, shell-type, toroidal (circular).

## Slide 18: Core-Type vs Shell-Type vs Toroidal
Core-type: windings on two limbs of rectangular core — common for power transformers.
Shell-type: core surrounds windings — better short-circuit strength and flux containment.
Toroidal: doughnut-shaped core — compact, low leakage flux, low noise, used in audio & precision equipment.

## Slide 19: Transformer Core Saturation
Saturation: when increasing magnetizing force (H) no longer increases flux density (B) linearly.
Causes: excessive flux (over-voltage), DC offset in supply, magnetizing current transients.
Effects: distorted output waveform, high magnetizing current, overheating, buzzing, increased losses.
Prevention: design margin (operate below knee of B–H curve), use proper core material, avoid DC on AC circuits, use air gap in some inductors.

## Slide 20: Transformer Losses & Efficiency
Loss types:
Copper losses (I2^22R): in windings, proportional to load2^22.
Core (iron) losses: frequency dependent
  Hysteresis loss — due to magnetisation cycles, ∝ frequency.
  Eddy current loss — induced currents in core, reduced by lamination.
Stray losses: leakage flux heating tank and supports.
Dielectric & mechanical losses (minor).
Typical efficiency: large power transformers ≈ 98–99% at rated load; small transformers lower.
Max efficiency occurs near rated load where copper loss ≈ core loss.

## Slide 21: Cooling Methods (Transformer Cooling)
Air-cooled (Dry type): natural air convection, used indoors/smaller units.
Oil-immersed (Liquid cooled):
ONAN — Oil Natural, Air Natural (natural convection of oil and air).
ONAF — Oil Natural, Air Forced (fans accelerate cooling).
OFAF / OFWF — Oil Forced, Air/Water Forced (pumps and heat exchangers).
Water-cooled: for very large units or special installations.
Cooling increases rating and life; oil also provides insulation.

## Slide 22: Transformer Types (Classification)
By Phase: Single-phase, Three-phase.
By Core Construction: Core-type, Shell-type, Toroidal.
By Cooling: Dry-type, Oil-immersed (ONAN, ONAF etc.), Water-cooled.
By Mounting / Location: Pole-mounted, Pad-mounted (ground), Substation (indoor/outdoor).
By Purpose: Power transformer, Distribution transformer, Instrument transformer (CT, PT), Isolation transformer, Autotransformer, Pulse transformer.

## Slide 23: By Installation / Location
Pole-mounted: outdoors on poles for rural distribution.
Pad-mounted: ground-mounted, fenced, used in residential/commercial areas.
Substation transformers: large, installed in substations (indoor/outdoor).
Indoor dry-type: in buildings, limited fire/safety hazards.

## Slide 24: Autotransformer (Special Type)
Single winding acts as both primary & secondary with taps.
Advantages: smaller, cheaper, lighter for same VA.
Disadvantages: not galvanically isolated (primary & secondary connected), limited voltage change range.

## Slide 25: Instrument Transformers: CT & PT
Current Transformer (CT):
Steps down high current to standard secondary (e.g., 5 A).
Used for metering and protection.
Accuracy depends on burden and class (e.g., 0.5, 1.0).
Potential/Voltage Transformer (PT/VT):
Steps down high voltage for meters/relays (e.g., 11 kV → 110 V).
Provides isolation and accurate voltage measurement.

## Slide 26: Applications of Transformers
Power distribution: step-up at generating stations, step-down near consumers.
Isolation: separate circuits for safety.
Impedance matching: audio systems and radio.
Measurement & protection: CTs and PTs for meters and relays.
Voltage stabilization: via tap changers.
Special: welding transformers, furnace transformers, SMPS transformers (high freq).

## Slide 27: Eddy Currents — Recap (with Prevention)
Induced in conducting parts where flux changes.
Problems: heating, energy loss, core noise.
Prevention: use laminated cores, insulated windings, slots, or ferrite cores at high frequencies.

## Slide 28: Parts of a Single-Phase Transformer
Core: Provides magnetic path for flux
Primary winding: Connected to input AC supply
Secondary winding: Connected to load; delivers transformed voltage
Insulation: Separates windings and prevents short circuits
Tank: Contains oil (in oil-filled types) and provides protection
Cooling system: Air-cooled or oil-cooled

## Slide 29: Parts of a Single-Phase Transformer
Conservator: Maintains oil level (oil transformers)
Breather: Removes moisture from air entering conservator
Bushings: Insulated terminals for HV and LV connections
Tap changer: Adjusts voltage ratio

## Slide 30: Transformer Core
Made of laminated silicon steel to reduce eddy current losses
Provides low reluctance path for alternating magnetic flux
Two main types:
Core type: Windings around two limbs
Shell type: Windings surrounded by core on three sides
Functions:
Carry alternating flux, Minimize losses, Improve coupling between windings

## Slide 31: Windings in a Transformer
Primary Winding
Connected to AC supply
Produces alternating magnetic flux in core
Current depends on input voltage and load on secondary
Secondary Winding
Receives magnetic flux and produces induced EMF
Supplies electrical load
Voltage depends on turns ratio

## Slide 32: Insulation in Transformer
Used to prevent electrical contact between windings and core
Materials:
  Paper insulation (kraft paper)
  Varnish
  Pressboard
  Transformer oil (insulating + cooling medium in oil-filled transformers)
Insulation must withstand:
  High voltage, Heat, Moisture, Mechanical stress

## Slide 33: Insulating Agents
Solid insulation: paper, cardboard, epoxy resin
Liquid insulation: transformer oil (mineral oil), synthetic oils
Gaseous insulation: air, SF₆ (for special transformers)
Functions:
  Provide dielectric strength
  Prevent short circuits
  Aid cooling (liquid insulation)

## Slide 34: EMF Equation of a Transformer

## Slide 35: Voltage Transformation Ratio (Turns Ratio)

## Slide 36: Current Ratio

## Slide 37: Magnetic Flux Path in a Single-Phase Transformer
AC current in primary → produces alternating flux in core
Flux links both windings
Induces EMF in secondary by mutual induction

## Slide 38: Practical Aspects of Transformer Models
Require high compute (GPUs/TPUs) for training
Scales extremely well with model size
Training dominated by matrix multiplications
Sensitive to batch size, learning rate, and tokenization quality
Memory usage grows with sequence length² (self-attention cost)
Used in: NLP, vision, speech, genomics, multimodal tasks

## Slide 39: Transformer Architecture (High-Level)
Encoder: Processes input sequence
Decoder: Generates output sequence (e.g., translation)
Each block contains:
Multi-Head Self Attention (MHSA)
Layer Normalization
Feed Forward Network (FFN)
Residual / skip connections
Fully parallelized — no recurrence, no convolution

## Slide 40: Model Size (Parameters & Scaling)
Controlled by:
Number of layers (depth)
Hidden dimension (width)
Attention heads
Feed-forward size (usually 4× hidden dim) Small: <100M parameters (BERT-base: 110M)Medium: ~1–10B parameters
Large-scale: 10B–1T+ parameters
Performance improves predictably with scale (scaling laws)

## Slide 41: Attention Masks
Padding mask:
Prevents model from attending to padded tokens
Causal/Decoder mask:
Prevents looking ahead into future tokens
Used for autoregressive (GPT-style) models
Encoder–decoder mask:
Controls cross-attention in seq2seq models

## Slide 42: Positional Encoding
Transformers have no recurrence, so need positional info.
Two types:
1. Sinusoidal Positional Encoding (Original)
Deterministic,Can extrapolate to longer sequences,Uses sine/cosine functions of different wavelengths
2. Learned Positional Embeddings
Trainable parameters, Adapt better to dataset structure, Limited to max sequence used during training

## Slide 43: AC (Alternating Current) — Introduction

## Slide 44: Types of AC Circuits
Resistive (R) – only resistors
Inductive (L) – only coils
Capacitive (C) – only capacitors
RC – resistor + capacitor
RL – resistor + inductor
RLC – resistor + inductor + capacitor

## Slide 45: Pure Resistive Circuit (R)

## Slide 46: Pure Inductive Circuit (L)
Current lags behind voltage by 90°
Voltage rises first, current comes later.
Inductor opposes change in current.

## Slide 47: Pure Capacitive Circuit (C)
Current leads voltage by 90°
Voltage rises after current.
Capacitor stores energy in electric field.

## Slide 48: RL Circuit (Resistor + Inductor)

## Slide 49: RC Circuit (Resistor + Capacitor)
Combines resistance and capacitance
Current leads voltage, but not full 90°

## Slide 50: RLC Series Circuit

## Slide 51: Reactance (Opposition to AC)

## Slide 52: Impedance (Z)