## Slide 1: Applied Science
Fsc Medical Technology
Awais Hamza

## Slide 2: Impurities in Water
Impurities: Substances present in water other than H₂O molecules. They affect taste, color, odor, conductivity, hardness, and safety.
Types of Impurities:
Physical impurities
Chemical impurities
Biological impurities

## Slide 3: Physical Impurities
Definition: Non-chemical contaminants that change the appearance of water.
Examples:
Suspended particles (sand, clay, silt), Turbidity
Color, odor, taste, Floating organic matter
Effects:
Make water look dirty, Increase turbidity
Cause foul smell/taste

## Slide 4: Chemical Impurities
Dissolved chemical substances that alter the composition of water.
Common Examples:
Dissolved salts (Ca²⁺, Mg²⁺, Fe²⁺)
Acids, bases, Industrial chemicals, Pesticides and fertilizers
Effects:
Change hardness
Make water unsafe for drinking
May cause poisoning or corrosion in pipes

## Slide 5: Biological Impurities
Living organisms present in water.
Examples:
Bacteria (E. coli, cholera bacteria), Algae
Viruses, Protozoa
Effects:
Cause diseases
Alter taste and odor
Can grow in stagnant water

## Slide 6: Hard and Soft Water
Soft Water: Water that forms easily lather with soap. Contains low concentration of Ca²⁺ and Mg²⁺ ions.
Hard Water: Water that does not lather easily with soap. Contains high levels of Ca²⁺ and Mg²⁺ ions.
Reason: Soap reacts with Ca²⁺/Mg²⁺ to form insoluble scum, reducing lather.

## Slide 7: Causes of Hardness
Hardness is caused mainly by:
1. Calcium salts
Calcium bicarbonate: Ca(HCO₃)₂, Calcium sulfate: CaSO₄
Calcium chloride: CaCl₂
2. Magnesium salts
Magnesium bicarbonate: Mg(HCO₃)₂, Magnesium sulfate: MgSO₄, Magnesium chloride: MgCl₂
Why these cause hardness?
Ca²⁺ and Mg²⁺ ions react with soap to form insoluble calcium/magnesium stearates, preventing foam formation.

## Slide 8: Types of Hardness
Hardness is classified into two main types:
1. Temporary Hardness
Caused by bicarbonates of calcium and magnesium
Removed by boiling
2. Permanent Hardness
Caused by sulfates and chlorides of Ca and Mg
Cannot be removed by boiling

## Slide 9: Removing Temporary Hardness
1. Boiling
Converts bicarbonates → carbonates + CO₂
Carbonates precipitate out Example: Ca(HCO₃)₂ → CaCO₃↓ + CO₂ + H₂O
2. Clark’s Method (Lime Softening)
Add calcium hydroxide (lime)
Precipitates CaCO₃ and Mg(OH)₂

## Slide 10: Removing Permanent Hardness
1. Washing Soda Method
Add Na₂CO₃, Precipitates CaCO₃ and MgCO₃ Example: CaSO₄ + Na₂CO₃ → CaCO₃↓ + Na₂SO₄
2. Ion-Exchange (Permutit/Zeolite Method)
Hard water passes through sodium zeolite, Ca²⁺/Mg²⁺ exchanged with Na⁺
Produces soft water
3. Synthetic Resins Method
Uses cation-exchange resins (R–Na), Ca²⁺/Mg²⁺ replaced with Na⁺ or H⁺

## Slide 11: Disadvantages of Hard Water
Poor lather formation with soap → more soap required
Forms scum with soap (insoluble Ca/Mg salts),Causes scale deposits in kettles, boilers, heaters, and pipes
Reduces efficiency of water heaters due to scale insulation
Causes blockage of pipes and decreases water flow, Leaves white spots on utensils, tiles, and bathroom fittings
Makes laundry stiff and dull; damages fabric over time, Interferes with industrial processes (dyeing, textile, paper)
Affects taste and may leave bitterness, Causes skin dryness and dull hair due to mineral deposits