## Slide 1: Applied Science- Chemistry
Fsc Medical Technology
Awais Hamza

## Slide 2: Soft & Hard Water
Soft Water
Contains very low dissolved salts.
Forms lather easily with soap.
No scum formation.
Hard Water
Contains high amounts of Ca²⁺ and Mg²⁺ ions.
Does not lather easily; forms scum with soap.
Causes scale in kettles, boilers, and pipes.

## Slide 3: Causes of Hardness in Water
Hardness is mainly caused by dissolved:
Calcium salts: Ca(HCO₃)₂, CaCl₂, CaSO₄
Magnesium salts: Mg(HCO₃)₂, MgCl₂, MgSO₄
Main sources:
Rocks & soil (limestone, chalk, gypsum)
Industrial waste
Groundwater passing through mineral-rich areas

## Slide 4: Reactions of CaCO₃ & MgCO₃ with CO₂ + H₂O
In presence of carbon dioxide and water:
Calcium carbonate reaction: CaCO₃ (s) + CO₂ (g) + H₂O (l) → Ca(HCO₃)₂ (aq) Soluble – causes temporary hardness
Magnesium carbonate reaction: MgCO₃ (s) + CO₂ (g) + H₂O (l) → Mg(HCO₃)₂ (aq) Soluble – causes temporary hardness

## Slide 5: Types of Hardness
Temporary Hardness
Due to bicarbonates of Ca and Mg
Ca(HCO₃)₂, Mg(HCO₃)₂
Removed by boiling
Permanent Hardness
Due to chlorides and sulfates
CaCl₂, MgCl₂, CaSO₄, MgSO₄
Cannot be removed by boiling

## Slide 6: Removal of Temporary Hardness
1. Boiling
Ca(HCO₃)₂ → CaCO₃ ↓ + CO₂ ↑ + H₂O Mg(HCO₃)₂ → Mg(OH)₂ ↓ + CO₂ ↑
Solid CaCO₃ and Mg(OH)₂ precipitate out → hardness removed.
2. Clark’s Method (Lime Treatment)
Add Ca(OH)₂ (slaked lime)
Converts bicarbonates into insoluble carbonates
Precipitates out CaCO₃ and MgCO₃

## Slide 7: Removal of Permanent Hardness
Permanent hardness cannot be removed by boiling. Main methods:
1. Washing Soda (Sodium Carbonate)
Na₂CO₃ + Ca²⁺ → CaCO₃ ↓ + 2Na⁺ Na₂CO₃ + Mg²⁺ → MgCO₃ ↓ + 2Na⁺ Insouble carbonates precipitate → hardness removed.

## Slide 8: Removal of Permanent Hardness
2. Sodium Zeolite / Permutit Method
Zeolite = sodium aluminosilicate
Exchange process: Ca²⁺ + Na₂Z → CaZ + 2Na⁺ Mg²⁺ + Na₂Z → MgZ + 2Na⁺
Removes both Ca²⁺ and Mg²⁺ completely
Produces soft water continuously

## Slide 9: Disadvantages of Hard Water
Poor lather formation → more soap required
Formation of scum with soap
Scale deposits in boilers, heaters, pipes
Reduces efficiency of appliances
Causes blockage and corrosion in pipes
Not suitable for dyeing, laundry, and chemical industries
Bad taste in drinking water (sometimes)

## Slide 10: The Water Cycle
Also called Hydrologic Cycle
Continuous movement of water on, above, and below Earth’s surface
Sun is the main driving force
Cycle includes evaporation, condensation, precipitation, and collection

## Slide 11: Main Stages of the Water Cycle
Evaporation
Condensation
Precipitation
Collection / Runoff
Additional processes:
Transpiration (from plants)
Infiltration (into ground)
Sublimation (ice → vapor)

## Slide 12: Evaporation
Process where liquid water changes into water vapor
Caused by heat from the sun
Occurs in:
  Oceans
  Rivers & lakes
  Wet soil
Transpiration: plants lose water vapor through leaves

## Slide 13: Condensation
Water vapor rises and cools down
Converts into tiny droplets of liquid water
Forms clouds and fog
Condensation releases heat into the atmosphere

## Slide 14: Precipitation
When cloud droplets combine and become heavy
They fall back to Earth as:
Rain
Snow
Hail
Sleet
Depends on temperature and atmospheric conditions

## Slide 15: Collection (Runoff + Storage)
After precipitation, water collects in:
Rivers & lakes
Oceans (largest collection)
Glaciers & ice caps
Underground aquifers (through infiltration)
Water then returns to evaporation → cycle continues.