## Slide 1: RIT
Fsc RIT
Awais Hamza

## Slide 2: Interaction of X-rays & Gamma Rays with Matter
High-energy photons meeting atoms
Foundation of radiography, nuclear physics & radiation protection 🜁 Think of photons as tiny messengers that stir atoms when they pass by.

## Slide 3: Key Factors Affecting Interaction
Photon energy (low vs high kVp)
Atomic number (Z) of the material
Density of the absorber
Thickness of the material

## Slide 4: Photoelectric Effect
Photon transfers all energy to an inner-shell electron
Electron is ejected → photoelectron
Vacant shell filled → produces characteristic radiation
Dominates in low energies & high-Z materials (bone)

## Slide 5: Compton Scattering
Photon hits an outer-shell electron
Electron kicked out → recoil electron
Photon deflected with less energy
Dominates in soft tissue at medium energies

## Slide 6: Pair Production
Only occurs when photon energy > 1.02 MeV
Photon vanishes → creates electron + positron
Positron later annihilates → produces two 0.51 MeV photons

## Slide 7: Coherent (Thomson/Rayleigh) Scatter
Low-energy photon vibrates entire atom
Photon leaves with same energy but changed direction
No ionization

## Slide 8: Photodisintegration
Very high-energy gamma photons (>10 MeV)
Photon absorbed by nucleus → nucleus emits a fragment (neutron/proton)

## Slide 9: Relative Importance (Diagnostic Range: 30–150 kVp)
Interaction | Importance
Photoelectric | Strong in bone (↑ contrast)
Compton | Dominant in soft tissue (↓ contrast)
Coherent | Minimal
Pair Production | None
Photodisintegration | None

## Slide 10: Comparison: X-ray vs Gamma Rays
Feature | X-rays | Gamma Rays
Origin | Electron shell | Atomic nucleus
Typical energy | keV | MeV
Medical use | Imaging | Therapy & nuclear medicine
Interactions | Mostly PE + Compton | Pair production + photodisintegration at high energies