## Slide 1: Cardiac Event Monitor
ADNAN RAMZAN
FSC(OT)

## Slide 3: Cardiac Event Monitor
Small wearable device to record heart rhythm over time
Detects abnormal rhythms that don’t happen daily
Works like ECG but for long-term monitoring
Battery-powered and portable
Notes: a standard cardiac monitor (like a Holter) records continuously (24/7) for a short period (days), while a cardiac event monitor is worn longer (weeks) but only records when you press a button or it detects an issue, capturing specific symptomatic episodes rather than constant data

## Slide 4: Types of Cardiac Event Monitors
Patch Recorder
patch recorder (or cardiac patch monitor) is a small, adhesive, wireless device worn on the chest to continuously record your heart's electrical activity (ECG) for days or weeks
worn for up to 2 weeks
Symptom Event Monitor – activated by patient when symptoms start
Loop Memory Monitor – records before & after events
Implanted Loop Recorder – under the skin for years
Notes: implantable loop recorder (ILR) is a small device that a healthcare provider places in your chest, just beneath the skin. It monitors your heart rate and rhythm and records anything that's abnormal. Most stay implanted for up to three years, but it may come out sooner if your provider gets the information they need.
insert or fix (tissue or an artificial object) in a person's body, especially by surgery.

## Slide 5: When is It Used?
Symptoms that happen rarely
Irregular heartbeats not seen in hospital
To diagnose hidden cardiac issues
To monitor heart over weeks/months

## Slide 6: Reasons for Use
Fainting, chest pain, dizziness
Palpitations After heart attack or stroke
Risk of arrhythmia
Notes: Heart palpitations (pal-pih-TAY-shuns) are feelings of having a fast-beating
(fainting)fast onset, short duration, and spontaneous recovery
irregularities in the heartbeat,

## Slide 7: Cardiac Event Monitor vs Holter Monitor
Feature | Holter Monitor | Event Monitor
Duration | 24–48 hours | Weeks to months
Recording | Continuous | Only during symptoms
Use | Frequent symptoms | Rare symptoms

## Slide 8: What is a Cardiac Monitor?
Bedside monitor showing heart’s electrical activity
Used in hospitals (ICU, OT, ER)
Provides continuous real-time readings

## Slide 9: Purpose of Cardiac Monitor
Shows ECG waves continuously
Measures oxygen saturation & blood pressure
Alerts staff if readings become abnormal
Helps emergency detection and treatment

## Slide 10: Components
Monitor screen
ECG cables & electrodes
Pulse oximeter probe
Blood pressure cuff

## Slide 11: Additional Easy Points
Improves patient safety
Helps doctors make quick decisions
Reduces hospital stay & complications
Patient-friendly, safe and painless

## Slide 12: Cardiac Event Monitor
Device used to record heart rhythms for a long duration
Helps diagnose irregular heartbeat conditions
Used in OPD / home settings

## Slide 13: How it Works
Sensors placed on chest
Detect and record heart’s electrical signals
Data sent to doctor by phone or computer
Doctor checks for abnormal heart rhythm

## Slide 14: What to Expect During Use
Sticky strips (electrodes) attached to chest
Painless and safe
You can bathe but may need to change patches
May need to press a button when symptoms occur

## Slide 15: What Results Show
Detects:
Tachycardia → fast heart rate
Bradycardia → slow heart rate
Atrial fibrillation
Atrial flutter Helps doctor plan treatment
Notes: Atrial flutter –organize manner
Atrial fib-------chaotic manner

## Slide 16: Do’s & Don’ts (Safety Precautions)
Keep monitor away from:
Electric blankets, razors
Mobile phones & magnets
Microwave ovens
Metal detectors

## Slide 17: Advantages of Cardiac Event Monitor
Helps detect hidden heart rhythm problems
Continuous monitoring at home
No hospital stay required
Cost-effective diagnosis method

## Slide 18: What is a Defibrillator?
A medical device used to treat life-threatening cardiac arrhythmias
Conditions: Ventricular fibrillation & Pulseless ventricular tachycardia
Delivers an electric shock to heart muscles
Restores normal heart rhythm and conduction
Life-saving emergency equipment

## Slide 20: How Defibrillation Works
Detects abnormal heart rhythm
Delivers controlled electrical shock
Heart momentarily stops to reset rhythm
Normal heartbeat restarts after shock

## Slide 21: Types of Defibrillators
External Defibrillators
Transvenous Defibrillators
Implantable Defibrillator (ICD)
AED – Automated External Defibrillator

## Slide 22: Uses of Defibrillator
Cardiac arrest
Severe arrhythmias
Emergency OT and ICU care
During heart surgeries