## Slide 1: Reactance, Resonance and Impedence
Fsc RIT
Awais Hamza

## Slide 2: Why Reactance & Impedance Matter
• AC current continuously changes direction • Circuit components oppose AC current differently than DC • Opposition to AC is not just resistance • This opposition is called impedance

## Slide 3: Basic AC Circuit Components
Three main components affect AC current:
• Resistor (R) – opposes current equally in AC & DC • Inductor (L) – opposes change in current • Capacitor (C) – opposes change in voltage

## Slide 4: What is Reactance?
Reactance (X)
• Opposition offered only to AC current • Caused by inductors and capacitors • Depends on frequency of AC • Measured in ohms (Ω)
⚠️ Reactance does not dissipate power, it stores energy temporarily

## Slide 5: Types of Reactance
There are two types:
• Inductive Reactance (XL) • Capacitive Reactance (XC)
They behave oppositely with frequency

## Slide 6: Inductive Reactance (XL)
Definition
• Opposition offered by an inductor to AC current • Due to magnetic field formation
Why it occurs
• Inductor resists change in current • Increasing current → induces back EMF

## Slide 7: Formula of Inductive Reactance
XL = 2πfL
Where: • f = frequency (Hz) • L = inductance (Henrys)
📌 As frequency increases → XL increases

## Slide 8: Behavior of Inductive Reactance
• At low frequency → XL is small • At high frequency → XL is large • At DC (f = 0) → XL = 0
➡ Inductor behaves like short circuit for DC

## Slide 9: Phase Relation in Inductor
• Current lags voltage by 90° • Voltage leads current
📌 Mnemonic: “ELI” → E leads I in Inductor

## Slide 10: Capacitive Reactance (XC)
Definition
• Opposition offered by a capacitor to AC current • Due to charge storage on plates

## Slide 11: Formula of Capacitive Reactance
XC = 1 / (2πfC)
Where: • f = frequency (Hz) • C = capacitance (Farads)
📌 As frequency increases → XC decreases

## Slide 12: Behavior of Capacitive Reactance
• At low frequency → XC is large • At high frequency → XC is small • At DC (f = 0) → XC = infinite
➡ Capacitor behaves like open circuit for DC

## Slide 13: Phase Relation in Capacitor
Current leads voltage by 90° • Voltage lags current
“ICE” → I leads E in Capacitor

## Slide 14: Comparison: XL vs XC
• XL ∝ frequency • XC ∝ 1 / frequency • XL increases with frequency • XC decreases with frequency • Phase behavior is opposite

## Slide 15: What is Impedance (Z)?
• Total opposition to AC current • Combination of: – Resistance (R) – Reactance (X)
• Measured in ohms (Ω)

## Slide 16: Impedance Formula
Z = √(R² + X²)
Where: • X = net reactance • X = XL − XC
Used in RLC circuits

## Slide 17: Impedance in Different Circuits
• Pure resistor → Z = R • Pure inductor → Z = XL • Pure capacitor → Z = XC • RLC circuit → combination of all

## Slide 18: What is Resonance?
Resonance
• Condition when: Inductive reactance = Capacitive reactance XL = XC
• Net reactance becomes zero

## Slide 19: Resonant Frequency
Resonant Frequency (fr)
fr = 1 / (2π√LC)
At resonance: • Circuit behaves like pure resistor • Impedance is minimum (series circuit) • Current is maximum

## Slide 20: Series Resonance
• XL = XC • Z = R (minimum) • Current is maximum • Power factor = 1 • Used in tuning circuits

## Slide 21: Parallel Resonance
• Impedance is maximum • Current is minimum • Used in filters and oscillators

## Slide 22: Frequency Response at Resonance
Below resonance → circuit is capacitive • At resonance → purely resistive • Above resonance → circuit is inductive

## Slide 23: Power at Resonance
• Maximum power transfer • Voltage and current in phase • No reactive power loss