## Slide 1: Radiography Imaging and Techniques
Fsc RIT
Awais Hamza

## Slide 2: Fluorescence
Immediate emission of light when exposed to X-rays
Stops instantly when exposure ends
Used in intensifying screens
Converts X-ray energy → visible light

## Slide 3: Phosphorescence
Delayed emission of light after exposure
Light continues even after X-rays stop
Causes image blur (fogging)
Not desirable in diagnostic imaging

## Slide 4: Difference (Fluorescence vs Phosphorescence)
Feature | Fluorescence | Phosphorescence
Duration | Instant | Delayed
After exposure | Stops immediately | Continues
Image quality | Sharp | Blurred
Use | Useful | Undesirable

## Slide 5: Absorption & Excitation
Absorption: Phosphor absorbs X-ray energy
Excitation: Electrons move to higher energy level
When electrons return → energy released as light

## Slide 6: Uses of Fluorescence
Intensifying screens (film radiography)
Fluoroscopy imaging
Reduces patient dose
Improves image visibility

## Slide 7: Uses of Phosphorescence
Rarely used in radiography
Seen in:
  Old imaging materials
  Glow-in-the-dark substances
Avoided in diagnostic imaging due to image degradation

## Slide 8: Intensifying Screen
Contains phosphor crystals
Converts X-rays → visible light
Light exposes film instead of direct X-rays
Advantage: Less radiation dose

## Slide 9: Care of Cassette
Keep clean and dry
Avoid dust → prevents image artifacts
Handle gently → avoid physical damage
Ensure proper screen-film contact
Store in cool, dry place

## Slide 10: Cleaning of Screens
Keep clean and dry
Avoid dust → prevents image artifacts
Handle gently → avoid physical damage
Ensure proper screen-film contact
Store in cool, dry place

## Slide 11: Common Errors
Dirty cassette → white spots/artifacts
Poor contact → blurred image
Phosphorescence → fogging
Damaged screen → image distortion