## Slide 1: Electrotherapy
FSC PT TECHNIQUE 1
DR DANISH NADEEM

## Slide 2: INTERFERENTIAL CURRENT
Allows deeper and more comfortable penetration Produces low frequency effect in targeted tissue - *Alternating Current:* Amplitude modulated medium-frequency current (2,000-5,000 Hz) - *Use two channels of differing carrier frequencies* to create a “beat” frequency within the tissues

## Slide 3: INTERFERENTIAL CLINICAL BENEFITS
Comfortable
Targeting hard to reach the tissues (e.g subscapularis)
Pain modulation
Acute pain
Chronic pain

## Slide 4: High Frequency
High Frequency Treatment: - This treatment can be applied directly or indirectly. - To the skin and can be used to heal, stimulate or sanitise the skin. - The machine uses a high frequency current that alternates over 100,000 cycles per seconds.

## Slide 5: Continued
- The output of the machine is a high frequency, alternating/oscillating current. - Frequency: 250,000 Hz. - Characteristics: - High voltage. - Low current flow. - The high frequency machine will have: - An on/off switch. - An intensity control.

## Slide 6: Types
- *High frequency treatment overview* - Uses a glass electrode applied directly onto the skin or over a layer of gauze. - Current passes through the electrode and is dispersed with slow circular motions. -Indirect high frequency treatment overview* - Client holds the electrode in their hands. - Therapist uses their hands to apply massage to the client’s skin. - Causes current to transfer from the client’s skin to the therapist’s hands. - *Frequency Detail* - Frequency of 60Hz

## Slide 7: Types of Electrodes
Mushroom electrode

## Slide 8: Continued
Flattened dome electrode

## Slide 9: Continued
Horseshoe electrode

## Slide 10: Continued
Roller electrode

## Slide 11: Continued
Fulgurator

## Slide 12: INTERFERENTIAL Therapy (IFT)
- Utilizes the significant physiological effects of low frequency (≈<250pps) electrical stimulation of nerves. - Aims to stimulate nerves without the associated painful and somewhat unpleasant side effects sometimes associated with low frequency stimulation.

## Slide 13: Electrodiagnosis
Electrodiagnosis is a medical diagnostic technique that uses electrical impulses to assess and evaluate the function of nerves, muscles, and the nervous system.
Common electrodiagnostic tests include: 1. Electromyography (EMG) 2. Nerve Conduction Studies (NCS) 3. Electroencephalography (EEG)

## Slide 14: ANY QUESTION